## Slide 1
4m Wind Tunnel, Warton, Lancashire
  Facility overview
  Built at Weybridge in 1950 and relocated to Warton in 1989-1991
  Working section size: 4.0m x 2.7m x 7.6m (13ft 1in x 8ft 10in x 24ft 11in)
  Tunnel pressurisation: Ambient stagnation pressure
  Maximum flow speed: M = 0.3
  Operating temperature: Ambient temperature
  Main drive fan: 1.3MW (1,740hp) AC motor 24ft diameter, 7 fixed pitch blades 410 rpm max
  Contraction ratio of 10.6:1
Primarily used for stability and control measurements, powered models and intake tests
Notes: Copyright © 2005 BAE Systems. All rights reserved.

## Slide 2
4m Wind Tunnel, Warton, Lancashire
  Instrumentation
  Sting or Strut Mounting Systems
  2 floor mounted (1 active) and 1 roof mounted turntables
  6-component balance:
    Aerotech weigh beam balance (under floor)
    Strain gauges and load cells
    Calibration rig & hardware
  Model Pressure Measuring Systems
    digital multi-pressure measurement systems (Scanivalve MPS, Chell nanoDAQ)
    Pressure Transducers (Druck, Kulite, Endevco)
  Flow visualisation: smoke, tufting and oil flows
  Common expandable DAS with flexible data visualisation systems
  Ground effect testing
  PIV
  Engine face rake measurements (6” Static + Swirl / Dynamic)
Notes: Copyright © 2005 BAE Systems. All rights reserved.

## Slide 3
4m Wind Tunnel, Warton, Lancashire
  Tunnel operations
  Test team consisting of engineers experienced in aerodynamics, instrumentation, design, manufacture, computing, mechanical and electrical
  Flexible working arrangements around 37hrs. Normal tunnel operation between 07:00 – 18:30 (20:20 on shift working)
  Pluses / minuses
  Successful repair of CFC blades to allow running to recommence following a 7 month activity
  Active recruitment of junior engineers
  Condition Monitoring of Fan Blades (blade deflection, Vibration sensors)
  Aging facilities requiring more maintenance and repair work to operate
  Loss of key experienced personnel and use of legacy in-house developed software
  Rolling Rig capability lost when the 5.5mLSWT closed in 2010
Notes: Copyright © 2005 BAE Systems. All rights reserved.