## Slide 1: Oxford’s Hypersonic Test Facilities
NWTF Tunnel Managers Meeting. 15th November 2023.
Chris Hambidge.

## Slide 2: The Hypersonics Group
Southwell Laboratory / Oxford Thermofluids Institute
Around 200 Students and Staff
Established 1960s – Heat Transfer
Rolls Royce UTC
1 Mile outside Oxford Centre
70% - 15% - 15%
Academic Industrial Industrial
Project Project Service
80% - 20%
Experimental Numerical
TRL: 1 2 3 4 5
Tunnel Team
Hypersonics
2013: Group Created
2014: NWTF Funding
2016: 1 Academic, 1 post-doc, 2 PhD students
2023: 7 Academics, 6 post-docs, 22 PhD students,
2 research engineers, Tunnel Team

## Slide 3: The Tunnels
High Density Tunnel
T6 Stalker Tunnel
Low Density Tunnel
2x Tier 1 NWTF Tunnels HDT & T6
1x Tier 2 NWTF Tunnel LDT
1x NWTF+ Hypersonic Tunnel HQT
4x Smaller Hypersonic Facilities CDST, CXT, OPG1 & OPG2

## Slide 4: High Density Tunnel (HDT)
  Constructed & Commissioned: 2014-2016
  Shots to date: 3350 [1 Shot/hour]
  Typical test campaign: 2-4 weeks
  Mach: 4 – 7, Nozzle Exit 350mm. +M3*
  P0 max = 275 bar, T0 max =550K
  Typical Operating Range: 20-100bar, 500K
  Typical Reu: 5x106 to 100x106/m
  Steady Test Periods: 3-7 of 30 to 50ms.
  Plenum Augmented Ludwieg Mode (PALM).
  → 2s ‘steady’ test time.
  → Expense of P0
  Light Isentropic Compression Heating (LICH) → T0 up to 1200k
  → Expense of P0 and Test Time
Heated Ludwieg Tunnel

## Slide 5
High Density Tunnel (HDT)
High-Speed Schlieren up to 1.75 Mfps
Focussed Laser Differential Interferometry (FLDI)
Laser Induced Grating Spectroscopy (LIGS)
Pressure Sensitive Paint (single and two colour)
Fast Response Pressure Sensors (Kulite and PCB)
High-Speed MWIR up to 1 Mfps
Bespoke Thin Film Heat Transfer Gauges
Free-Flight Inertial Force Measurement
High-Speed Motion Tracking up to 1.75 Mfps
Fast-Response Force Balances: 1x 6DOF, 2x 4DOF.
Bespoke Scramjet Mass Capture Device
Bespoke Shear Measurement Device
Secondary Gas Injection System + Mass Flow Control
Two-Axis Traverse
Rakes/Plates/Cones
Scramjet Dynamics
Transition Mechanisms
Transpiration Cooling
Heat Flux Augmentation
(Patterned Roughness, Engineering Features)
Flight Dynamics
Scramjet Intake Testing
Free-Flight Testing
Bespoke Heat Transfer Gauges
Elliptical Cone Model (HiFire 5)

## Slide 6
High Density Tunnel (HDT)
Scramjet Dynamics
Transition Mechanisms
Transpiration Cooling
Heat Flux Augmentation
(Patterned Roughness, Engineering Features)
Flight Dynamics
Scramjet Intake Testing
Free-Flight Testing
Bespoke Heat Transfer Gauges
Elliptical Cone Model (HiFire 5)

## Slide 7
The Stalker Tunnel (T6)
  Constructed & Commissioned: 2014 - 2018
  Shots to date: 500 [1 Shot/day]
  Typical test campaign: 4-6 weeks
  Nozzles: M7, M8, M10, Nozzle Exit 96 to 280mm.
  Flow Speed: up to 18km/s
  Operating Range
  1,500 K < T0 < 20,000 K
    10 MPa < P0 < 1000 Mpa
  Flow Duration: 2 μs to 5 ms.
Free-Piston Driven Multi-Mode Shock Tunnel
  Mode 2: (Aluminium) Shock Tube*
    → Low carbon contamination
    → Boundary layer effects reduced
  → Max Speed 12 km/s
  → Test Time 2-50 μs
  Mode 4: Reflected Shock Tunnel
  → Max Speed 6.5 km/s
  → Test Time 1-5 ms
  Mode 3: Expansion Tube/Tunnel*
  → Max Speed 12 km/s
  → Test Time 50-500 μs
  Mode 1: Straight Through
  Shock Tube*
  → Max Speed 18 km/s
  → Test Time 2-50 μs

## Slide 8
Sub-scale Galileo model tested at
18.0 km/s for Neptune entry (84.5% H2 / 15% He / 0.5% CH4).
Double-cone model tested in Expansion Tunnel mode
at 6.3 km/s (19.8 MJ/kg) for earth entry.
Visible, Near-IR Spectroscopy
Vacuum Ultra-Violet Spectroscopy
Atmosphere Gas Composition Matching (Inc Flammable gas)
LEO Return ~11km/s
Mars Return ~16km/s
Gas Giant Entry ~19km/s (*30km/s)
Bespoke Diamond Heat Transfer Gauges
The Stalker Tunnel (T6)
Non-Equilibrium Thermochemistry
Planetary Entry Aerothermodynamics
Satellite demise, Planetary Probes, Capsules
Inter-Facility Comparisons (EAST) & CFD Validation
Satellite demise heat transfer testing at 6.5 km/s for LEO return.
Non-Equilibrium Flow behind a shock wave at
7.3 km/s for Mars entry (95.8% CO2 / 4.2% N2)

## Slide 9
The Stalker Tunnel (T6)
Non-Equilibrium Thermochemistry
Planetary Entry Aerothermodynamics
Satellite Demise, Planetary Probes, Capsules
Inter-Facility Comparisons (EAST)
& CFD Validation
Sub-scale Galileo model tested at
18.0 km/s for Neptune entry (84.5% H2 / 15% He / 0.5% CH4).
Double-cone model tested in Expansion Tunnel mode
at 6.3 km/s (19.8 MJ/kg) for earth entry.
Satellite demise heat transfer testing at 6.5 km/s for LEO return.
Non-Equilibrium Flow behind a shock wave at
7.3 km/s for Mars entry (95.8% CO2 / 4.2% N2)

## Slide 10: Low Density Tunnel
  Recommissioned: 2014-2016
  Rebuilding capability
  Mach: 6, Nozzle Exit 108mm, core flow 36mm
  1.5 m Diameter Test Section.
  T0 max =523K
  Continuous Operation
  Kn 0.0005 to 1 for L=10mm
Continuum
Slip
Transition
Free-Molecular
L=10mm
High Altitude Aerothermodynamics
Satellite Demise
Planetary Surface Analogy (Mars)
Raw camera image of upper-stage satellite analogue coated with a 3-temperature liquid crystal slurry at Ma = 5.8, Kn ≈ 0.02.
Magnetic suspension balance (subject of NWTF+)

## Slide 11: Strengths/Challenges
Strengths:
Unique Capabilities
Range Test Capabilities In One Place
Affordable Hypersonic Ground Testing
Training of Future Experts
Access to Expertise
Challenges:
Short Duration (Instrumentation Complexity & Cost)
Wide Operational Pressure Range (High Pressure to Medium/High Vacuum)
Capacity (Short Test Slots with Regular Reconfiguration)
Space (inc. Co-location of T6 & HDT)
Recruiting and Maintaining Staff
Bootstrapping a Professional Service