## Slide 1: 5m Wind Tunnel, Farnborough, Hampshire
  Facility overview
  Built in the 1970s – first run 1977
  Working section size: 5m x 4.2m x 12.2m (16ft 5in x 13ft 9in x 40ft)
  Tunnel pressurisation: atmosphere to 300kPa (43.5psi)
  Maximum flow speed: M = 0.33 at atmosphere M = 0.27 at 300kPa
  Operating temperature: 20 - 30°C (68 - 86°F)
  Main drive fan: 11MW (14,750hp) AC motor 1.6MW (2,200hp) DC motor 10m diameter, 10 fixed pitch blades 310 rpm max
Primarily used for take-off and landing configuration development for commercial aircraft.

## Slide 2: 5m Wind Tunnel, Farnborough, Hampshire
  Instrumentation
  Precision pressure gauges for tunnel control
  6-component Loads measurement:
  Underfloor weighbeam balance
  Several internal strain gauge balances
  Underfloor load cell balance (undergoing refurbishment)
  Balance Calibration Machine
  Model & tunnel walls pressure measurements.
  3x TE Measurement Specialties Optimus systems
  iMetrum Model Deformation Measurement system (new)
  Flow visualisation : minitufts and oil flows
  Ground effect testing
  Acoustics measurements
  PIV (external system providers used)

## Slide 3: 5m Wind Tunnel, Farnborough, Hampshire
  Tunnel operations
  Test team of ~26 people
  Aerodynamics, computing, instrumentation, mechanical & electrical engineers
  2 shifts per day operation for most tests (06:00 – 22:30)
  Pluses / minuses
  First UK test for the global High-Lift Common Research Model initiative in 2019
  New 5mWT-sized full-span model will be tested in 2024
  Plans to continue expanding facility capability, including further development of electric motor powered aeroengine simulators
  Plan to continue forging closer ties within the UK for collaborative working opportunities – dependent upon funding
  Ageing workforce and facility will require large investment.